## Slide 2: Lab 2 – Truss Design
2D truss code

## Slide 3: Example
FE = 1000 N
1
2
3
4
1
2
3
4
5
1, 2, 3, and 4 are the joints
1
,
2
3
4
5
,
,
, and
are the members
Assume length of each member is the same for this example.
x
y

## Slide 4: Method of Joint – FBD for each joint
FE
1
2
3
4
F# = magnitude of force in member #
R3
R2
R = Reaction force at support
R1
F1
F1
F2
F2
F5
F5
F4
F4
F3
F3
-u1
u1
u2
-u2
u3
-u5
u5
-u3
-u4
u4
x
y
u1
= -i
For this system
u2
= -j
u3
= cos 45° i
- sin 45° j
u4
= i
u5
= j
= u3x i + u3y j

## Slide 5: Equilibrium of Joint 1
FE
1
F1
F5
Equilibrium of Joint 2
2
F1
F2
F3
u1
-u5
-u1
u2
u3
… (i)
… (ii)
… (iii)
… (iv)

## Slide 6: Equilibrium of Joint 3
Equilibrium of Joint 4
3
R1
F2
F4
-u2
u4
4
R3
R2
F5
F4
F3
u5
-u3
-u4
… (v)
… (vi)
… (vii)
… (viii)

## Slide 7
No. of equations = 2 x no. of joint … since we have 2 equations at each joint
… (i)
… (ii)
… (iii)
… (iv)
… (v)
… (vi)
… (vii)
… (viii)
No. of members + No. of reactions
No. of unknowns =
2 x 4 = 8
5 + 3 = 8
Solve using solve using matrices

## Slide 8: Assemble the system of linearly independent equations
… (i)
… (ii)
… (iii)
… (iv)
… (v)
… (vi)
… (vii)
… (viii)
F1
F2
F3
F4
F5
R1
R2
R3
External
Sum
-F1
-FE
= 0
Joint 1 x-dirn
Joint 1 y-dirn
Joint 2 x-dirn
Joint 2 y-dirn
Joint 3 x-dirn
Joint 3 y-dirn
Joint 4 x-dirn
Joint 4 y-dirn
-F5
= 0
F1
cos45°F3
= 0
-F2
-sin45°F3
= 0
F4
= 0
F2
R1
= 0
-F4
-cos45°F3
R3
= 0
F5
sin45°F3
R2
= 0

## Slide 9: Assemble the system of linearly independent equations
… (i)
… (ii)
… (iii)
… (iv)
… (v)
… (vi)
… (vii)
… (viii)
F1
F2
F3
F4
F5
R1
R2
R3
External
-F1
= FE
Joint 1 x-dirn
Joint 1 y-dirn
Joint 2 x-dirn
Joint 2 y-dirn
Joint 3 x-dirn
Joint 3 y-dirn
Joint 4 x-dirn
Joint 4 y-dirn
-F5
= 0
F1
cos45°F3
= 0
-F2
-sin45°F3
= 0
F4
= 0
F2
R1
= 0
-F4
-cos45°F3
R3
= 0
F5
sin45°F3
R2
= 0
Can write in matrix form! A x = b

## Slide 10: Assemble the system of linearly independent equations
F1
F2
F3
F4
F5
R1
R2
R3
-1
FE
Joint 1 x-dirn
Joint 1 y-dirn
Joint 2 x-dirn
Joint 2 y-dirn
Joint 3 x-dirn
Joint 3 y-dirn
Joint 4 x-dirn
Joint 4 y-dirn
-1
0
1
cos45°
0
-1
-sin45°
0
1
0
1
1
0
-1
-cos45°
1
0
1
sin45°
1
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
=
A
x
b
=

## Slide 11: A systematic approach
Things we need to know: (i.e. the things in the input file)
1. Location of the joint
2. Which members are connected to which joint - connectivity
3. Where are the reaction and what are there components
4. Where are the external forces and what are there components
Joint # | x-coordinate | y-coordinate
1 | X1 = L | Y1 = L
2 | X2 = 0 | Y2 = L
3 | X3 = 0 | Y3 = 0
4 | X4 = L | Y4 = 0
Member # | From joint | To joint
1 | 1 | 2
2 | 2 | 3
3 | 2 | 4
4 | 3 | 4
5 | 4 | 1
Location of joints
Connectivity
Joint # | x-component direction | y-component direction
3 | 0 | 1
4 | 0 | 1
4 | 1 | 0
Reactions
External Forces
Joint # | x-component | y-component
1 | -FE = 1000 N | 0

## Slide 12: Dealing with force directions – ‘From’ joints and ‘To’ joints
‘From’ joint
‘To’ joint
(XF,YF)
(XT,YT)
Unit vector for ‘From’ joint
uFrom =
(XT – XF) i + (YT - YF) j
Unit vector for ‘To’ joint
uTo =
(XF – XT) i + (YF - YT) j
Member N

## Slide 13: Steps to create A-matrix
Start at joint 1:
Assuming that the input information in the tables have been read and stored
Member # | From joint | To joint
1 | 1 | 2
2 | 2 | 3
3 | 2 | 4
4 | 3 | 4
5 | 4 | 1
Connectivity
Members 1 and 5 are connected at joint 1.
Note whether joint is a ‘From’ or ‘To’ joint for each member
Joint 1 is a ‘From’ joint for member 1
Joint 1 is a ‘To’ joint for member 5
Form the unit vector for each member force at the joint
Means we are dealing with the 1st and 2nd rows of the A-matrix
Get the members that are connected to joint 1.
Enter coefficients of unknown member force first.
Note the joint that connects to the other end of each member
Member 1 is connected to joint 2
Member 5 is connected to joint 4

## Slide 14: Steps to create A-matrix
Form the unit vector for each member force at the joint
Unit vector for ‘From’ joint
uFrom =
(XT – XF) i + (YT - YF) j
If join is a ‘From’ joint use:
Otherwise it is a ‘To’ joint, so use:
Unit vector for ‘To’ joint
uTo =
(XF – XT) i + (YF - YT) j
Joint 1 is a ‘From’ joint for member 1
Thus we can fill in the 1st and 2nd row entries in the A-matrix for the F1 column
u1,1 =
(X2 – X1) i + (Y2 – Y1) j
u1,1 =
(0 – L) i + (L – L) j
Joint # | x-coordinate | y-coordinate
1 | X1 = L | Y1 = L
2 | X2 = 0 | Y2 = L
3 | X3 = 0 | Y3 = 0
4 | X4 = L | Y4 = 0
Location of joints
u1,1 =
(-1) i + (0) j
i.e. Row 1 - Joint 1 x-direction
Column 1 - force F1 column
Coefficient = -1
i.e. Row 2 - Joint 1 y-direction
Column 1 - force F1 column
Coefficient = 0
joint
Member

## Slide 15: Steps to create A-matrix
Joint 1 is a ‘To’ joint for member 5
Thus we can fill in the 1st and 2nd row entries in the A-matrix for the F5 column
u1,5 =
(X4 – X1) i + (Y4 – Y1) j
u1,5 =
(L – L) i + (0 – L) j
Joint # | x-coordinate | y-coordinate
1 | X1 = L | Y1 = L
2 | X2 = 0 | Y2 = L
3 | X3 = 0 | Y3 = 0
4 | X4 = L | Y4 = 0
Location of joints
u1,5 =
(0) i + (-1) j
i.e. Row 1 - Joint 1 x-direction
Column 5 - force F5 column
Coefficient = 0
i.e. Row 2 - Joint 1 y-direction
Column 5 - force F5 column
Coefficient = 1

## Slide 16: Steps to create A-matrix
At joint 2:
Member # | From joint | To joint
1 | 1 | 2
2 | 2 | 3
3 | 2 | 4
4 | 3 | 4
5 | 4 | 1
Connectivity
Members 1, 2, and 3 are connected at joint 2.
Note whether joint is a ‘From’ or ‘To’ joint for each member
Joint 2 is a ‘To’ joint for member 1
Joint 2 is a ‘From’ joint for member 2
Form the unit vector for each member force at the joint
Means we are dealing with the 3rd and 4th rows of the A-matrix
Get the members that are connected to joint 2.
Note the joint that connects to the other end of each member
Member 1 is connected to joint 1
Member 2 is connected to joint 3
Next, move to joint 2
Joint 2 is a ‘From’ joint for member 3
Member 3 is connected to joint 4

## Slide 17: Steps to create A-matrix
Form the unit vector for each member force at the joint
Unit vector for ‘From’ joint
uFrom =
(XT – XF) i + (YT - YF) j
If join is a ‘From’ joint use:
Otherwise it is a ‘To’ joint, so use:
Unit vector for ‘To’ joint
uTo =
(XF – XT) i + (YF - YT) j
Joint 2 is a ‘To’ joint for member 1
Thus we can fill in the 3rd and 4th row entries in the A-matrix for the F1 column
u2,1 =
(X1 – X2) i + (Y1 – Y2) j
u2,1 =
(L – 0) i + (L – L) j
Joint # | x-coordinate | y-coordinate
1 | X1 = L | Y1 = L
2 | X2 = 0 | Y2 = L
3 | X3 = 0 | Y3 = 0
4 | X4 = L | Y4 = 0
Location of joints
u2,1 =
(1) i + (0) j
i.e. Row 3 – Joint 2 x-direction
Column 1 - force F1 column
Coefficient = 1
i.e. Row 4 – Joint 2 y-direction
Column 1 - force F1 column
Coefficient = 0

## Slide 18: Steps to create A-matrix
Joint 2 is a ‘From’ joint for member 2
Thus we can fill in the 3rd and 4th row entries in the A-matrix for the F2 column
u2,2 =
(X3 – X2) i + (Y3 – Y2) j
u2,2 =
(0 – 0) i + (0 – L) j
Joint # | x-coordinate | y-coordinate
1 | X1 = L | Y1 = L
2 | X2 = 0 | Y2 = L
3 | X3 = 0 | Y3 = 0
4 | X4 = L | Y4 = 0
Location of joints
u2,2 =
(0) i + (-1) j
i.e. Row 3 – Joint 2 x-direction
Column 2 - force F2 column
Coefficient = 0
i.e. Row 4 – Joint 2 y-direction
Column 2 - force F2 column
Coefficient = -1

## Slide 19: Steps to create A-matrix
Joint 2 is a ‘From’ joint for member 3
Thus we can fill in the 3rd and 4th row entries in the A-matrix for the F3 column
u2,3 =
(X4 – X2) i + (Y4 – Y2) j
u2,3 =
(L – 0) i + (0 – L) j
Joint # | x-coordinate | y-coordinate
1 | X1 = L | Y1 = L
2 | X2 = 0 | Y2 = L
3 | X3 = 0 | Y3 = 0
4 | X4 = L | Y4 = 0
Location of joints
u2,3 =
(1/√2 ) i + (-1/√2) j
i.e. Row 3 – Joint 2 x-direction
Column 3 - force F3 column
Coefficient = 1/√2
i.e. Row 4 – Joint 2 y-direction
Column 3 - force F3 column
Coefficient = -1/√2

## Slide 20: Steps to create A-matrix
At joint 3:
Member # | From joint | To joint
1 | 1 | 2
2 | 2 | 3
3 | 2 | 4
4 | 3 | 4
5 | 4 | 1
Connectivity
Members 2, and 4 are connected at joint 3.
Note whether joint is a ‘From’ or ‘To’ joint for each member
Joint 3 is a ‘To’ joint for member 2
Joint 3 is a ‘From’ joint for member 4
Form the unit vector for each member force at the joint
Means we are dealing with the 5th and 6th rows of the A-matrix
Get the members that are connected to joint 3.
Note the joint that connects to the other end of each member
Member 2 is connected to joint 2
Member 4 is connected to joint 4
Next, move to joint 3

## Slide 21: Steps to create A-matrix
Form the unit vector for each member force at the joint
Unit vector for ‘From’ joint
uFrom =
(XT – XF) i + (YT - YF) j
If join is a ‘From’ joint use:
Otherwise it is a ‘To’ joint, so use:
Unit vector for ‘To’ joint
uTo =
(XF – XT) i + (YF - YT) j
Joint 3 is a ‘To’ joint for member 2
Thus we can fill in the 5th and 6th row entries in the A-matrix for the F2 column
u3,2 =
(X2 – X3) i + (Y2 – Y3) j
u3,2 =
(0 – 0) i + (L – 0) j
Joint # | x-coordinate | y-coordinate
1 | X1 = L | Y1 = L
2 | X2 = 0 | Y2 = L
3 | X3 = 0 | Y3 = 0
4 | X4 = L | Y4 = 0
Location of joints
u3,2 =
(0) i + (1) j
i.e. Row 5 – Joint 3 x-direction
Column 2 - force F2 column
Coefficient = 0
i.e. Row 6 – Joint 3 y-direction
Column 2 - force F2 column
Coefficient = 1

## Slide 22: Steps to create A-matrix
Joint 3 is a ‘From’ joint for member 4
Thus we can fill in the 5th and 6th row entries in the A-matrix for the F4 column
u3,4 =
(X4 – X3) i + (Y4 – Y3) j
u3,4 =
(L – 0) i + (0 – 0) j
Joint # | x-coordinate | y-coordinate
1 | X1 = L | Y1 = L
2 | X2 = 0 | Y2 = L
3 | X3 = 0 | Y3 = 0
4 | X4 = L | Y4 = 0
Location of joints
u3,4 =
(1) i + (0) j
i.e. Row 5 – Joint 3 x-direction
Column 4 - force F4 column
Coefficient = 1
i.e. Row 6 – Joint 3 y-direction
Column 4 - force F4 column
Coefficient = 0

## Slide 23: Steps to create A-matrix
At joint 4:
Member # | From joint | To joint
1 | 1 | 2
2 | 2 | 3
3 | 2 | 4
4 | 3 | 4
5 | 4 | 1
Connectivity
Members 3, 4, and 5 are connected at joint 4.
Note whether joint is a ‘From’ or ‘To’ joint for each member
Joint 4 is a ‘To’ joint for member 3
Joint 4 is a ‘To’ joint for member 4
Form the unit vector for each member force at the joint
Means we are dealing with the 7th and 8th rows of the A-matrix
Get the members that are connected to joint 4.
Note the joint that connects to the other end of each member
Member 3 is connected to joint 2
Member 4 is connected to joint 3
Next, move to joint 4
Joint 4 is a ‘From’ joint for member 5
Member 5 is connected to joint 1

## Slide 24: Steps to create A-matrix
Form the unit vector for each member force at the joint
Unit vector for ‘From’ joint
uFrom =
(XT – XF) i + (YT - YF) j
If join is a ‘From’ joint use:
Otherwise it is a ‘To’ joint, so use:
Unit vector for ‘To’ joint
uTo =
(XF – XT) i + (YF - YT) j
Joint 4 is a ‘To’ joint for member 3
Thus we can fill in the 7th and 8th row entries in the A-matrix for the F3 column
u4,3 =
(X2 – X4) i + (Y2 – Y4) j
u4,3 =
(0 – L) i + (L – 0) j
Joint # | x-coordinate | y-coordinate
1 | X1 = L | Y1 = L
2 | X2 = 0 | Y2 = L
3 | X3 = 0 | Y3 = 0
4 | X4 = L | Y4 = 0
Location of joints
u4,3 =
(-1/√2) i + (1/√2) j
i.e. Row 7 – Joint 4 x-direction
Column 3 - force F3 column
Coefficient = -1/√2
i.e. Row 8 – Joint 4 y-direction
Column 3 - force F3 column
Coefficient = 1/√2

## Slide 25: Steps to create A-matrix
Joint 4 is a ‘To’ joint for member 4
Thus we can fill in the 7th and 8th row entries in the A-matrix for the F4 column
u4,4 =
(X3 – X4) i + (Y3 – Y4) j
u4,4 =
(0 – L) i + (0 – 0) j
Joint # | x-coordinate | y-coordinate
1 | X1 = L | Y1 = L
2 | X2 = 0 | Y2 = L
3 | X3 = 0 | Y3 = 0
4 | X4 = L | Y4 = 0
Location of joints
u4,4 =
(-1) i + (0) j
i.e. Row 7 – Joint 4 x-direction
Column 4 - force F4 column
Coefficient = -1
i.e. Row 8 – Joint 4 y-direction
Column 4 - force F4 column
Coefficient = 0

## Slide 26: Steps to create A-matrix
Joint 4 is a ‘From’ joint for member 5
Thus we can fill in the 7th and 8th row entries in the A-matrix for the F5 column
u4,5 =
(X1 – X4) i + (Y1 – Y4) j
u4,5 =
(L – L) i + (L – 0) j
Joint # | x-coordinate | y-coordinate
1 | X1 = L | Y1 = L
2 | X2 = 0 | Y2 = L
3 | X3 = 0 | Y3 = 0
4 | X4 = L | Y4 = 0
Location of joints
u4,5 =
(0) i + (1) j
i.e. Row 7 – Joint 4 x-direction
Column 5 - force F5 column
Coefficient = 0
i.e. Row 4 – Joint 2 y-direction
Column 5 - force F5 column
Coefficient = 1

## Slide 27: Steps to create A-matrix
Reaction 1 is at joint 3:
Means we are dealing with the 5th and 6th rows of the A-matrix
We are dealing with the R1 column, i.e. column 6
Next, enter coefficients for the reactions
Joint # | x-component direction | y-component direction
3 | 0 | 1
4 | 0 | 1
4 | 1 | 0
Reactions
We can fill in the 5th and 6th row entries in the A-matrix for the R1 column
i.e. Row 5 – Joint 3 x-direction
Column 6 – force R1 column
Coefficient = 0
i.e. Row 6 – Joint 3 y-direction
Column 6 – force R1 column
Coefficient = 1

## Slide 28: Steps to create A-matrix
Reaction 2 is at joint 4:
Means we are dealing with the 7th and 8th rows of the A-matrix
We are dealing with the R2 column, i.e. column 7
Joint # | x-component direction | y-component direction
3 | 0 | 1
4 | 0 | 1
4 | 1 | 0
Reactions
We can fill in the 7th and 8th row entries in the A-matrix for the R2 column
i.e. Row 7 – Joint 4 x-direction
Column 7 – force R1 column
Coefficient = 0
i.e. Row 8 – Joint 4 y-direction
Column 7 – force R1 column
Coefficient = 1

## Slide 29: Steps to create A-matrix
Reaction 3 is at joint 4:
Means we are dealing with the 7th and 8th rows of the A-matrix
We are dealing with the R3 column, i.e. column 8
Joint # | x-component direction | y-component direction
3 | 0 | 1
4 | 0 | 1
4 | 1 | 0
Reactions
We can fill in the 7th and 8th row entries in the A-matrix for the R2 column
i.e. Row 7 – Joint 4 x-direction
Column 8 – force R3 column
Coefficient = 1
i.e. Row 8 – Joint 4 y-direction
Column 8 – force R3 column
Coefficient = 0

## Slide 30: Steps to create b-matrix
External Force is at joint 1:
Means we are dealing with the 1st and 2nd rows of the b-matrix
Enter the know external forces
We can fill in the 1st and 2nd row entries in the b-matrix:
i.e. Row 1 – Joint 1 x-direction
Value = -1000
i.e. Row 2 – Joint 1 y-direction
Value = 0
External Forces
Joint # | x-component | y-component
1 | -FE = -1000 N | 0